## Slide 1
CT-216
CONVOLUTIONAL CODES
Presented By :
Lab Group 3 Sub-group 1
DAIICT | 2024

## Slide 2
DAIICT | 2024
  We declare that,
  The work we are presenting here is our own work, that we have done in a group.
  We have not copied any part of the whole code or result from someone's code or codes given on the internet.
  Concepts, understanding and insights we will be describing are our own.
  We make this pledge truthfully. We know that violation of this solemn pledge can carry grave consequences.
  Wherever we have relied on an existing work that is not our own, we have provided a proper reference citation.
Honor Code

## Slide 3
Signatures
DAIICT | 2024
1

## Slide 4
DAIICT | 2024
2
  The main source of our code and concepts is the material posted on Google Classroom.
  We used sources like some videos of NPTEL and other YouTube Videos.
  Books which we used :
  J. G. Proakis. Digital Communications. 4th edition. McGraw-Hill, 1995.
  Dasari Sai Bhargav. Viterbi Decoding for Convolutional Codes.
Acknowledgement of any help

## Slide 5
Outline
DAIICT | 2024
3
  History
  Introduction to convolutional codes
  Convolutional encoder
  Convolutional codes representation and explanation with examples
-Generator Representation
-State Diagram Representation
-Trellis Diagram Representation
  Decoding of convolutional codes
-Viterbi algorithm
  Theoretical Analysis
  Conclusion

## Slide 6
DAIICT | 2024
4
History
  Convolutional coding was first introduced in 1955 by Peter Elias. Initially, it was believed that these codes could be decoded with high accuracy, albeit at the cost of increased computation and delay.
  However, in 1967, Andrew Viterbi discovered that convolutional codes could be decoded with maximum-likelihood using trellis-based decoders, thus introducing the Viterbi algorithm.
  Subsequent to this, other decoding algorithms based on trellises, such as the BCJR algorithm, were developed.
Andrew Viterbi

## Slide 7
DAIICT | 2024
5
Problem Statement
  Reason for using Convolutional Codes:
  In contrast to Block Codes, the Convolutional Codes work by encoding a continuous stream of information rather than discrete blocks.
  These codes rely on memory, using previous bits to encode or decode subsequent ones. Within the Convolutional Coding, the output bits are calculated through logical operations involving the current bit in the stream and a limited number of preceding bits.
  The Convolutional codes find use in applications where achieving high performance with minimal implementation complexity, often utilizing shift registers, is essential.

## Slide 8
DAIICT | 2024
6
  Implement convolutional encoding with varying constraint lengths and code rates.
  Modulate the encoded data using BPSK modulation.
  Simulate transmission through an AWGN channel with varying SNR level.
  Analyze and understand the difference in performance of soft decision and hard decision decoding methods under different SNR conditions.
Objectives

## Slide 9
DAIICT | 2024
7
AWGN
  Additive white Gaussian noise (AWGN) is characterized by being additive, having a constant power spectral density across frequencies (white), and following a Gaussian probability distribution.
  The mean of AWGN is typically zero(0) and the variance of AWGN Is 𝜎2. And it is denoted by N(0, 𝜎2).
  Probabilty distribution of AWGN :
(source : sfu.ca )

## Slide 10
DAIICT | 2024
8
BPSK
  BPSK stands for Binary Phase Shift Keying. It is a digital modulation scheme used in communication systems to transmit binary data (0s and 1s) over a communication channel.
  A phase shift of 0 degrees is used to represent one symbol (e.g., 0), and a phase shift of 180 degrees (or π radians) is used to represent the other symbol (e.g., 1)
Image source: https://www.researchgate.net/figure/BPSK-modulation-and-constellation-diagram_fig1_338542687

## Slide 11
  Typically convolution codes are characterized or described as [n,k,Kc].
  The incoming stream of bits is broken into segments of k bits and passed through the encoder, which n output bits.
  These n output bits are generated by n generator polynomials with each generator polynomial having length Kc, where Kc is called constraint length.
  The memory of the encoder is m, where m= Kc- k.
  For the given encoder, the code rate is defined as r=k/n.
  Further implementation and structure of encoder on : next slide
Encoder Concept
DAIICT | 2024
9

## Slide 12
DAIICT | 2024
10
Encoder Structure
Here is an encoder with Kc= 3 , n = 3 , k= 1
g1 = [1 1 0] , g2 = [1 0 1] , g3 = [1 1 1 ]
|
|
image source: https://www.ee.iitb.ac.in/~sarva/courses/EE605/2014/slides/ViterbiAlgorithm.pdf

## Slide 13
DAIICT | 2024
11
State Diagram Representation
image source: https://www.ee.iitb.ac.in/~sarva/courses/EE605/2014/slides/ViterbiAlgorithm.pdf

## Slide 14
  There are many decoding algorithms for the Convolutional code like Viterbi Algorithm, BCJR Algorithm (Bahl-Cocke-Jelinek-Raviv Algorithm), Fano Algorithm,Sequential Decoding Algorithms.
  We will discuss only Viterbi algorithm .
Decoder Concept
DAIICT | 2024
12

## Slide 15
  In Viterbi algorithm we use trellis data structure.
  We can do HDD ( Hard Decision Decoding ) or SSD ( Soft Decision Decoding).
  In case of , HDD we use Hamming Distance.
  In case of , SDD we use Euclidean Distance.
  Lets see the process of decoding using Viterbi algorithm.
  suppose we are using encoder which we have in slide 10.
Viterbi Algorithm
DAIICT | 2024
13

## Slide 16
  Suppose the received message is [110 110 110 111 010 101 101]
  Step 1 :
  Make a trellis from the state table.
  We will assume that the initial state is zero and the path will also terminate to the all-zeros state.
  So we will append 2 zeroes at the end of input so that it terminates at all-zeros state.
  The Trellis will be:
DAIICT | 2024
14
110
110
010
111
110
101
101
image source: https://www.ee.iitb.ac.in/~sarva/courses/EE605/2014/slides/ViterbiAlgorithm.pdf

## Slide 17
  Step 2:
    For each stage calculate Hamming Distance from previous stage’s stored values and store minimum for each state, discarding other paths.
DAIICT | 2024
15
110 110 110 111 010 101 101
Received Codeword:

## Slide 18
  Discarding non optimal path:
DAIICT | 2024
16
  At t=3, on state S0 there are two paths with cumulative hamming distance of 4 and 5, so we will discard the path having a hamming distance of 5, and we will do this for all states in trellis where there is more than 1 path.
110 110 110 111 010 101 101

## Slide 19
  Keep doing this till last stage , and you will get only one survivor path which is most likelihood for our trasmitted codeword.
DAIICT | 2024
17
110 110 110 111 010 101 101

## Slide 20
  Step 3 :
  Do backtracking and get the whole path.
  in backtracking we compute the sum of the previous path matric and hamming distance for all states from which we can reach our current state of the current stage and we select the state with the minimum sum, we will keep doing this till the end of loop iteration i.e. till first stage.
  After doing backtracking, we will have [111 010 110 011 111 101 011], Which has a minimum hamming distance from received message.
DAIICT | 2024
18
Here we have performed HDD by using hamming distance , similarly we can performe SDD by simply storing euclidean distance instead of hamming distance

## Slide 21
DAIICT | 2024
19
Transfer function
  Transfer function is an algebraic representation of all the paths that start and end with zero state.
Here ,
  Exponent of D ( d ) indicates the number of ones in output codeword.
  Exponent of N ( f(d) ) indicates the number of ones in input block k bits - at a time .
  Exponents of J ( g(d) ) indicates the number of branches spanned by the path.

## Slide 22
DAIICT | 2024
20
Method to calculate transfer function for given encode:
Encoder :
state diagram :
  First Draw the state diagram for given encoder.

## Slide 23
DAIICT | 2024
21
  Split state a ( zero state ) into two states a ( start ) and e ( end )
and compute weight of all branches for new state diagram.
  Write state equation for all states.

## Slide 24
DAIICT | 2024
22
  Transfer function T(D,N,J) =Xe/Xa
After solving ,
  The factor J is important if we are transmitting a sequence of finite duration.
  If we are transmitting an infinite length sequence , we may wish to suppress the dependence of T(D,N,J)
on the parameter J. this can be done by putting J=1;
in

## Slide 25
Theoretical Analysis

## Slide 26
  In this section, we will try to estimate an upper bound for the error probability with soft decision Viterbi decoding.
  For the simplicity of the derivation, we assume that all zero sequences are transmitted and we determine the probability of error in deciding in favor of another sequence.
  We define as the coded binary digit for the mth bit for the jth branch of the ith path in the trellis for convolution code, and rjm as the output of the demodulator for the corresponding mth bit of the jth branch, where rjm is:
DAIICT | 2024
23
Probability of Error For Soft Decision Decoding:

## Slide 27
  Where njm is represented as AWGN with mean 0 and variance 1, and εc is the transmitted signal energy for each code bit.
  The “Branch metric is defined for the jth branch of the ith path through the trellis as the logarithm of the joint probability of the sequence {rjm, m = 1, 2, 3} conditioned on the transmitted sequence {cjm, m = 1, 2, 3} for the ith path.
  Furthermore, “Path metric” for the ith path consisting of B branches through the trellis is defined as:
DAIICT | 2024
24

## Slide 28
  For the soft decision decoding, the channel adds AWGN to the signal.
  Probability of getting r (i) jm given c (i) jm is equal to probability of noise equal to
  Since noise is normally distributed, we can directly compute it using the formula for the probability density function of a normally distributed variable.
DAIICT | 2024
25

## Slide 29
  Correlation metric for the ith path is defined as sum of branch metric for that path.
  Suppose i=0 is all zero path and i=1 is another path that merge with all zero path after some transitions.
DAIICT | 2024
26
Correlation Metric :

## Slide 30
  We define the first-event error probability as the probability that another path merges with all zero path at node B which has metric that exceeds the matric of all zero path for the first time.
  Suppose the incorrect path has i=1, which merges with the all-zero path and differs from the all-zero path in d-bits.
  We define pairwise error probability as the probability of the correlation metric of the incorrect path being greater than the correct(all zero) path,
  Since the coded bits in two paths are identical except in d positions only d terms will left.
DAIICT | 2024
27
First event error probability:
The r ′l are the independent and identically distributed gaussian radnom variables with the mean − √ εc and variance No/2 .

## Slide 31
  Upon solving the previous equation we get, (proof for the same is given in the attached pdf)
  There are many possible paths with different distances that merge with the all-zero path at a given node B. We can sum the pairwise error probability over all paths to obtain an upper bound on the first-event error probability in the form
DAIICT | 2024
28
  Where ad denotes the number of paths of distances ‘d’ from the all-zero path that merges with the all-zero path for the first time.
  We can the upper bound of Q function using Chernoff bound as:
  Hence,
  Where γb= εb/N0 is received SNR per bit and Rc is code rate

## Slide 32
  If we multiply the pairwise error probability P2(d) by the number of incorrectly decoded information bits for the incorrect path at the node where they merge we obtain the bit error rate for that path.
  We know that the exponent in the factor N contained in the transfer function T(D,N) indicate the number of information bit errors in selecting an incorrect path that merges with all-zero path at some node B.
DAIICT | 2024
29
Bit error probability

## Slide 33
  We saw how to find first event error probability in SDD.
  Similarly we can find first event probability for Hard Decision Decoding.
Hard decision decoding
DAIICT | 2024
30

## Slide 34
  Bitwise error probability We assume that we transmit all-zero path.
  Suppose i=0 is all zero path and i=1 is another path that merges with all zero path after some transitions.
  Path i=1 contains d ones.
  So, if d is odd, path 1 will be chosen over path 0 if there are more than (d+1)/2 ones
  and if d is even, path 1 will be chosen over path 0 if there are more than d/2 ones and there is half probability that path 1 will be chosen when the number of 1’s equal to d/2.
DAIICT | 2024
31
Bitwise error probability

## Slide 35
  There are many possible paths with different distances that merge with the all-zero path at given node.
  Therefore, there is no simple exact expression for the first-event error probability.
  However, we can provide an upper bound as we did in SDD.
  We can provide an upper bound of P2(d) :
DAIICT | 2024
32

## Slide 36
  If we multiply the pairwise error probability P2(d) by the number of incorrectly decoded information bits for the incorrect path at the node where they merge we obtain the bit error rate for that path.
  We will use the transfer function to get information about the number of incorrectly decoded bits.
DAIICT | 2024
33

## Slide 37
DAIICT | 2024
34
RESULTS
SIMLUATION RESULT COMPARISON FOR THE DIFFRENT VALUES OF [n,k,Kc]

## Slide 38
DAIICT | 2024
35
RESULTS
SIMLUATION RESULT COMPARISON FOR THE DIFFRENT VALUES OF [n,k,Kc]

## Slide 39
DAIICT | 2024
36
RESULTS
SIMLUATION RESULT COMPARISON FOR THE DIFFRENT VALUES OF [n,k,Kc]

## Slide 40
  Beyond a certain point, decreasing R(CodeRate) too much can lead to inefficiency in the use of the channel bandwidth or resource, or it may adversely impact the overall throughput of the communication system.
  As the memory of the register increases, more number of previous input bits is used to encode each new bit.
  This additional information increases the accuracy and decreases BER for a given value of code rate for the encoded data.
  With higher Kc, the decoder can better detect and correct errors introduced during transmission due to noise, leading to a lower BER at a given signal-to-noise ratio(SNR)
  By taking the Euclidean distance between the expected and received voltages, we also take into account the information contained in the received bit where as in the hard decoding where we use a threshold voltage value to map received voltages to bits and therefore there is lose of information during the conversion. Therefore soft decision decoding provides better path metric and therefore is able to perform better than hard decoding.
Conclusion
DAIICT | 2024
37